CONTROL OF EQUIPMENT AND SYSTEM STATUS

1.0	Objective

The objective of this surveillance is to verify that the contractor has established and implemented an effective program to control equipment and system status.  The surveillance activities provide a basis for verifying the effectiveness of the contractor's program as well as compliance with DOE requirements.

2.0	References

2.1	DOE 5480.19, Conduct of Operations Requirements for DOE Facilities

2.2	DOE-STD-1039-93, Guide to Good Practices for Control of Equipment and System Status

3.0	Requirements Implemented

This surveillance is conducted to implement requirements of the Functions, Responsibilities and Authorities Manual, Section 20, Operations, FRAM #s 4253, 4258, and 4261.  These requirements are drawn from DOE 5480.19.

4.0	Surveillance Activities

Activity 1 -	The Facility Representative selects a component, system, or portion of a system that is out of service due to maintenance or testing activities.  The Facility Representative determines whether the status of that component or system has been accurately and consistently reflected in facility logs and status boards.  The Facility Representative determines whether operations personnel are aware of the status of the selected component or system.

Activity 2 -	The Facility Representative reviews the status of out-of-service alarms in the control area.

Surveillance Guideline

CONTROL OF EQUIPMENT AND SYSTEM STATUS

Surveillance No.:	_____________________________

Facility:		_____________________________

Date Completed:	_____________________________

Activity 1 -	Review of status of selected component or system

Yes  No   N/A

___  ___  ___	1.	Did the shift supervisor or appropriate authority approve the removal from service of the component or system?

DOE 5480.19, Attachment 1, Chapter 8, C. 1.

___  ___  ___	2.	Did the shift supervisor or appropriate authority sign the work authorization that removed the equipment from service?

DOE 5480.19, Attachment 1, Chapter 8, C. 6

.

___  ___  ___	3.	Is a signed copy of the work authorization maintained in the control area?

DOE 5480.19, Attachment 1, Chapter 8, C. 6.

___  ___  ___	4.	Is the component or system status accurately and consistently reflected in the shift supervisor's log, other operations logs, on equipment and system status boards, on shift turnover documentation, in the equipment deficiency log, in equipment and system alignment checksheets, and in the lockout and tagout log?

DOE 5480.19, Attachment 1, Chapter 8, C. 5.

___  ___  ___	5.	When applicable, do logs, status sheets, turnover checklists, and other appropriate documentation reflect entry into limiting conditions of operation and actions that are taken in response to technical safety requirements?

DOE 5480.19, Attachment 1, Chapter 8, C. 4.

___  ___  ___	6.	Are operations personnel aware of the status of the affected component or system and the actions being taken to restore the component or system to service?

DOE 5480.19, Attachment 1, Chapter 8, C. 1.

Yes  No   N/A

___  ___  ___	7.	Are the status of the affected component or system and the actions being taken to restore the component or system to service accurately communicated during shift turnover?

DOE 5480.19, Attachment 1, Chapter 8, C. 1.

___  ___  ___	8.	Are alignment checklists used to guide the operator in establishing the correct component positions when returning equipment to service?

DOE 5480.19, Attachment 1, Chapter 8, C. 2.

___  ___  ___	9.	Does operations shift supervision review and approve completed alignment checklists?

DOE 5480.19, Attachment 1, Chapter 8, C. 2.

___  ___  ___	10.	Is equipment tested following maintenance to demonstrate it is capable of performing its intended function?  Is the testing documented?

DOE 5480.19, Attachment 1, Chapter 8, C. 7.

___  ___  ___	11.	Is a system established to ensure that the operations personnel receive and utilize the latest revisions of engineering drawings and specifications?

DOE 5480.19, Attachment 1, Chapter 8, C. 10.

Activity 2 -	Review of the status of out-of-service alarms in the control area

___  ___  ___	12.	Are alarms that are partially or totally disabled identified and labeled through the use of the lockout/tagout system, equipment deficiency logs, or other appropriate documentation?

DOE 5480.19, Attachment 1, Chapter 8, C. 8

.

___  ___  ___	13.	Is the status of the maintenance work requests or other corrective actions periodically reviewed and reprioritized as necessary?

DOE 5480.19, Attachment 1, Chapter 8, C. 9

___  ___  ___	14.	Are backup instrumentation, measurements, and readings used when alarms are out of service, in accordance with approved procedures?

DOE 5480.19, Attachment 1, Chapter 8, C. 8

___  ___  ___	15.	Are operations personnel aware of the status of out-of-service alarms and of the status of corrective actions to restore the alarms to service?

DOE 5480.19, Attachment 1, Chapter 8, C. 5

OTHER:

NOTES/COMMENTS:

PERSONNEL CONTACTED:

FINDINGS:

Finding No.:

Description:

Finding No.:

Description:

OBSERVATIONS:

Observation No.:

Description:

FOLLOWUP ITEMS:

CONTRACTOR MANAGEMENT DEBRIEFED AND RESULTS:

Signature:  _______________________________	Date: _____/_____/_____

Facility Representative