Suspect/Counterfeit Items

Criteria Review and Approach Document (CRAD)

NNSA/Nevada Site Office Facility Representative Division

Phase 1 - Management

Performance Objective:

Management should have a formal system under Quality Assurance with adequate controls defined and implemented to identify and preclude Suspect/Counterfeit Items (S/CI) from being introduced into safety systems and applications that create potential hazards.

CRITERIA:

- Management should have a formal system of controls in place for assurance that all items procured meet the requirements for their intended use.

- Management should have a system of mechanisms to continuously maintain current, accurate, updated information on SC/Is and associated suppliers using all available sources.

- Management should have a training program with detailed records that ensures managers, supervisors, and workers of S/CI controls are being trained and informed on prevention, detection, and disposition of S/CIs.

- Management should ensure that the standards and methods used for determining the acceptability of items are continuously reviewed, and based on consensus standards and/or commonly accepted industry practices consistent with applicable law.

- Management should have S/CI controls that include Engineering involvement in the procurement process, notably in the development of specifications during inspection and testing and when replacing, maintaining, or modifying equipment.

- Management should have procurement procedures that preclude the introduction of S/CIs by: (1), identifying technical and QA requirements; (2), accepting only those items that comply with procurement specifications; and (3), inspecting inventory and storage areas to identify, control, and disposition S/CIs.

- Management should have testing methods approved by Engineering for the testing of procured or in-place S/CIs.

- Management should have routine maintenance cycles or inspection activities for their safety as well as non-safety systems that shall include provisions for the identification of S/CIs.

- Management, both federal and contractor, should have established policies and procedures using a government-wide system, Government/Industry Data Exchange Program (GIDEP), for exchanging information on nonconforming products and materials among other agencies.

- Management, both federal and contractor, should have specific procedures for receiving and disseminating S/CI information through their respective Inspectors General or other appropriate officers.

- Management, both federal and contractor, should notify their suppliers of nonconforming products in accordance with GIDEP procedures (in addition to the required actions specified in FAR Part 46.407).

References:

1.  10 CFR 830, Subpart A

2.   DOE/EH-0135, “Performance Objectives and Criteria for Technical Safety Appraisals at                      Department of Energy Facilities and Sites.”  June 1990

3.   BN CD-3200.004, “Suspect/Counterfeit Items Program.”  May 3, 2004

4.   DOE Order 221.1, “Reporting Fraud, Waste, and Abuse to the Office of Inspector General.”

5.   DOE Order 231.1-2, “Occurrence Reporting and Processing of Operations Information,” 	August 2003.

6.   DOE O 232.1A, “Occurrence Reporting & Processing of Operations Information.”  August 1,          1997

7.   DOE Order 414.1A, “Quality Assurance,” July 2001.

8.   DOE O 440.1A, “Worker Protection Management for DOE Federal and Contractor Employees.”

9.   DOE Guide 440.1-6, “Implementation Guide for use with Suspect/Counterfeit Items                         Requirements of DOE Order 440.1, ‘Worker Protection Management,’”

10. Office of Environment, Safety and Health Support Manual to the Process Guide for the                     Identification and Disposition of Suspect/Counterfeit of Defective Items at DOE Facilities.

11. IAEA-TECDOC-1169, “Managing suspect and counterfeit items in the nuclear industry,”                 August 2000.

APPROACH:

Document Review:

- Selected procedures

- Selected test documents and plans concerning S/CIs,

- Selected occurrence reports on S/CIs.

- Selected approved training plans.

- Selected Hot Line Permits / Work On Or Near Energized Equipment Permit

Observations:

- Selected work, testing, or training being performed including crew briefings, testing setup and/or conduct of testing, maintenance activities, or trouble-shooting activities.

Interviews:

- Selected Management personnel

- Selected maintenance, support and/or inspection staff

- Selected Trainers/Training Coordinators

Lines of Inquiry

SUSPECT/COUNTERFEIT ITEMS

NNSA/Nevada Site Office Facility Representative Division

Phase 1 - Management

|  | YES | NO | N/A | COMMENTS |
| --- | --- | --- | --- | --- |
| 1. Has management implemented a system, or controls, to assure the procurement of items designed to meet specified requirements for intended use? [DOE O 440.1A] |  |  |  |  |
| 2. Has management installed mechanisms to continuously maintain accurate, updated information on SC/Is and associated suppliers using all available sources? [DOE O 440.1A] |  |  |  |  |
| 3. Has management a training program, with detailed records, for training and informing managers, supervisors, and workers on controls for prevention, detection, and disposition of S/CIs? [DOE O 440.1A] |  |  |  |  |
| 4. Have all BN personnel, employees and management associated with S/CIs, completed BN Course No. 1N00A146, “Suspect/ Counterfeit Items Awareness?” [BN CD-3200.004] |  |  |  |  |
| 5. Have supervisors checked current training records for expired training? [DOE/EH-0135] |  |  |  |  |
| 6. Have the standards and methods used for determining the acceptability of items been reviewed (based on consensus standards or accepted industry practices consistent with applicable law)? [DOE O 440.1A] |  |  |  |  |
| 7. Do the S/CI controls include Engineering involvement in the procurement process (notably in the development of specifications during inspection and testing and when replacing, maintaining, or modifying equipment)? [DOE O 440.1A] |  |  |  |  |
| 8. Do procurement procedures identify technical and QA requirements that prevent the introduction of S/CIs? [DOE O 440.1A] |  |  |  |  |
| 9. Do the Property Management Representatives review the BN Intranet CA S/CIs Home Page to determine if a prospective supplier has been identified by the DOE as supplying S/CI? [BN CD-3200.004] |  |  |  |  |
| 10. Does the BN S/CI Coordinator keep the CA S/CIs Home Page updated with the latest S/CIs information? How often? [BN CD-3200.004] |  |  |  |  |
| 11. Does the BN S/CI Coordinator maintain a file of S/CIs alerts, occurrence reports, internal notifications, evaluations and investigations? [BN CD-3200.004] |  |  |  |  |
| 12. Do the procurement procedures accept only those items that comply with procurement specifications? [DOE O 440.1A] |  |  |  |  |
| 13. Do procurement procedures identify means or methods for inspecting inventory and storage areas to identify, control, and disposition S/CIs? [DOE O 440.1A] |  |  |  |  |
| 14. Are representative samples of procured materials being inspected before they are accepted (to verify conformance to specification and performance requirements)? [BN CD- 3200.004] |  |  |  |  |
| 15. Are “maintaining, inspecting, testing, and accepting records” traceable to the original Purchase Order (PO)? [BN CD- 3200.004] |  |  |  |  |
| 16. Does management have procedures on testing methods approved by Engineering for the testing of procured or in- place S/CIs? [DOE O 440.1A] |  |  |  |  |
| 17. Do the managers (Project, Operation, Facility and Support Services) identify, establish and maintain current lists of safety systems, equipment, or facilities? [BN CD-3200.004] |  |  |  |  |
| 18. Are there routine maintenance cycles or inspection activities for safety as well as non-safety systems that include provisions for identifying S/CIs? [DOE O 440.1A] |  |  |  |  |
| 19. Are S/CIs reported to GIDEP and the IG? [DOE O 231.1, DOE O 232.1A, DOE 2030.4B] |  |  |  |  |
| 20. Are trend analyses being conducted, and Lessons Learned issued for improving all S/CI activities? [DOE O 440.1A] |  |  |  |  |
| 21. Does management participate in the Government/Industry Data Exchange Program (GIDEP)? [OMB Policy Letter 91-3] |  |  |  |  |
| 22. Has management established, communicated, and implemented effective system policies or controls to assure the procurement of items in accordance with OMB Policy Letter 91-3? |  |  |  |  |
| 23. Are suppliers of nonconforming products or materials notified in accordance with GIDEP procedures? [OMB Policy Letter 91-3] |  |  |  |  |
| 24. Are suppliers of nonconforming products and materials being notified according to GiDEP procedures (as well as to the actions specified in FAR Part 46.407)? [OMB Policy Letter 91-3] |  |  |  |  |
| 25. Have the contractors and laboratories completed any assessments for S/CI during the previous 3 years? [NVO 220.XC] |  |  |  |  |
| 25. Have the corrective actions concerning S/CI found in previous assessments been implemented, and the findings closed with respect to caWeb? |  |  |  |  |
| 26. Have the SCI reported as Occurrence Reports in previous assessments been closed and reported to ORPs? |  |  |  |  |
| 27. Has an ALERT been sent out to other contractors and laboratories (procurers), and the IG been properly notified? |  |  |  |  |
| 28.. Have previously identified S/CI been verified as S/CI through further assessment? |  |  |  |  |
| 29. Have previously identified products or materials labeled as S/CI been exonerated as being S/CI? |  |  |  |  |