## Slide 1: Key Project Development and Financing Concepts

## Slide 2: Agenda
Levelized Cost of Energy (LCOE)
Electricity Offtakers
Project Roles
Tax Equity Partnerships

## Slide 3
Project Financing Concepts:
Levelized Cost of Energy
3

## Slide 4: Key Concept: Levelized Cost of Energy (LCOE)
Measures lifetime costs divided by energy production
Calculates present value of the total cost of building and operating a power plant over an assumed lifetime. Expressed in real or nominal dollars on a megawatt-hour (MWh) or kilowatt-hour (kWh) basis
Allows the comparison of different technologies (e.g., wind, solar, natural gas) of unequal life spans, project size, different capital cost, risk, return, and capacities
Critical to making an informed decision to proceed with development of a facility-, community-, or commercial-scale project
Notes: Look at Lantz PPT
Pull something from Transparent cost database, or picture instead of bullet #2 (to emphasize it – only if time permits)
Add CREST and SAM as tools (SAM wizard)
TP
-what is LCOE
-why we use it

## Slide 5: LCOE

## Slide 6
Adapted from European Wind Energy Association, “Economics of Wind Energy,” http://www.ewea.org/fileadmin/ewea_documents/documents/00_POLICY_document/Economics_of_Wind_Energy__March_2009_.pdf
Annual Expenses
Initial Costs Including Financing
Energy System
Annual Cost Per Year
Annual
Energy Production
LCOE
($/MWh)
× $$$
Site Characteristics/
Resources
$
Simple LCOE Concept
$

## Slide 7: LCOE and Cash Flows
Chart: Annual Costs ($/year)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Equity | 1000000 | 250000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Debt | 250000 | 245000 | 245000 | 245000 | 245000 | 245000 | 245000 | 245000 | 245000 | 295000 | 245000 | 245000 | 245000 | 245000 | 245000 | 0 | 0 | 0 | 0 | 0
Operating Expenses | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 175000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000 | 125000
Taxes | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000
LCOE | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110 | 110
Adapted from Black and Veatch “Levelized Cost of Energy Calculation”:
http://www.efchina.org/csepupfiles/report/20112844913435.70772110666485.pdf/Levelized%20Cost%20of%20Energy%20Calculation_BV_EN.pdf
Levelized Cost of Energy
Notes: [Note to slide presenter: consider matching legend colors to “approved graphics” Cash Flow Example slide]

## Slide 8: Using LCOE
Calculating and comparing LCOE can:
  Measure value across the longer term, showing probable life-cycle costs
  Highlight opportunities for Tribes to develop different scales of projects (facility, community, or commercial)
  Inform decisions to pursue projects on an economic basis, compared to utility rates
  Most renewable energy projects have zero fuel costs (with biomass being the possible exception)

## Slide 9: Wind LCOE Sensitivity: What Are the Big Drivers?
Initial capital cost (ICC) and capacity factor are two critical drivers, but discount rate (financing costs) and annual operating expenses (AOE) are non-trivial. Wind LCOE example shown below:
Source: Tegen et al. 2012
Notes: [Note to slide presenter, replace “framework” in slide title since we use that word to mean something else in another place in the course series.]

## Slide 10: Tribal Community Scale Example
A Tribe in Arizona has a remote facility not served by the grid. Diesel fuel is used to power generators to run 24/7.
Chart: Sample Cost of Energy Comparison (constant demand)
Diesel Power | 1.2578 | 1.3333 | 1.4133 | 1.4981 | 1.588 | 1.6833 | 1.7842 | 1.8913 | 2.0048 | 2.1251 | 2.2526 | 2.3877 | 2.531 | 2.6829 | 2.8438 | 3.0145 | 3.1953 | 3.387 | 3.5903 | 3.8057
Utility Power | 1.8127 | 1.8671 | 1.9231 | 1.9808 | 2.0403 | 2.1015 | 2.1645 | 2.2295 | 2.2963 | 2.3652 | 2.4362 | 2.5093 | 2.5845 | 2.6621 | 2.7419 | 2.8242 | 2.9089 | 2.9962 | 3.0861 | 3.1787
Renewable Power | 1 | 1.02 | 1.0404 | 1.0612 | 1.0824 | 1.1041 | 1.1262 | 1.1487 | 1.1717 | 1.1951 | 1.219 | 1.2434 | 1.2682 | 1.2936 | 1.3195 | 1.3459 | 1.3728 | 1.4002 | 1.4282 | 1.4568
Currently, grid tie appears more expensive than diesel generators
Immediate savings from new solar generation, including infrastructure
Savings could total ~$20M over 20 years
Calculations assumed tax equity used by third-party solar provider
Notes: IS THIS BASED ON AN ACTUAL ANALYSIS—WE NEED MORE INFO HERE.

## Slide 11
Project Financing Concepts:
Offtakers
11

## Slide 12: Step 1: Site and Project Potential Buyer
MAP KEY |  |  |  |  | 
WAPA TRANSMISSION, IN-SEVICE |  | TSGT TRANSMISSION, PROPOSED |  | IOU UTILIITY SERVICE AREA | 
WAPA TRANSMISSION, PROPOSED |  | Tribal UTILITY SERVICE AREA |  | STATE/MUNICIPAL UTILITIY SERVICE AREA | 
TSGT TRANSMISSION, IN-SERVICE |  | COOPERATIVE UTILITY SERVICE AREA |  |  | 
Identify and begin discussions with potential power purchasers in Arizona:
Navopache Electric Cooperative (NEC)
Salt River Project (SRP)
Arizona Public Service (APS)
Tucson Electric Power
Navajo Tribal Utility Authority (NTUA)
Notes: Slide 12
Let’s dig deeper into a few key aspects of our hypothetical example
As a first step, consider all of the entities that might want to purchase power in your area. Think of these entities as the customers of the power; without an offtaker a commercial scale renewable energy project most assuredly will not work.
Will they buy your power? Maybe, if they need the power and have a renewable energy requirement, but it also has to be at an attractive enough price to consider.
Here is an example of some of the different electricity service territories in the southwestern U.S.

## Slide 13
Project Financing Concepts:
Tax Equity Partnership
13

## Slide 14: Step 2: Ownership Structure Options
Direct ownership
Third-party power purchase agreement (PPA)
  Containing a traditional land lease/royalty structure
Equity investment partnering
  Partnership flip
  Sale leaseback
  Inverted lease/lease pass-through
Key Question: What viable ownership structure options are attractive to the community?
Notes: Slide 14
A key consideration is figuring out how to get the money to build a renewable project.
Several options to consider:
  Direct ownership, purchased with cash
  3rd party ownership under a power purchase agreement (the power is sold to the utility, and the Tribe gets royalties for the land), and
  Equity investment partnering, which can be done using various financing structures – which I will describe in detail
The Key question is: what viable ownership structure options are attractive to the community?

## Slide 15: So Why Seek a Tax-Equity Finance Partner?
Tax incentives (MACRS and either PTC or ITC) can represent up to half the project value or reduce project’s capital costs by ~50%
Tax incentives can help to achieve a competitive price of power
Many projects also require state-level incentives to be economically viable.
Chart: After Tax Project Capital Costs
| 3rd Party Owned | Tribe Owned (w/o Partner)
 | 50 | 100
Third-Party-Owned
Tribe-Owned (w/o Partner)
Notes: With and without tax incentives

## Slide 16
Project Financing Concepts:
Project Roles
16

## Slide 17: Key Concept: Tribal Role Options
Tribe
Renewable Resource/Land Owner/Land Lessor*
Off-taker (Power Purchaser/ User)
Lender/ Debt Provider
Equity Investor/ Generation Equipment Owner
Project Developer
Project Operator/O&M
* Also called Tribal Host
Notes: Slide 17
This graphic shows the full list of project development roles that a Tribe can potentially play for a commercial scale renewable power project. Notice that between the previous slide and this one, a few roles dropped off that are really most appropriate for other project partners.
Each of the roles that a Tribe can play at the commercial scale level are different in nature, between the level of involvement on a short and long term basis, the level of risk at stake, the potential upside of the project, and the degree of control of the project and team.

## Slide 18: Discussion: Questions and Answers
Notes: JASON – Can you have some questions in your back pocket in case no one has questions ?