## Slide 1: The Value of CSP With Storage
And cost reduction opportunities
CSP SunShot Program Summit
April 2016
Bill Gould
Chief technical officer
solarreserve

## Slide 2: Within the Rapidly Growing Renewable Energy Market, Solar Thermal with Integrated Storage Plays a Key Role
Global energy market context
  The installed capacity of renewable energy is forecast to more than double by 2025 to reach 3,203 GW or 39% of global installed capacity
  The highest share of total renewable energy capacity additions is expected to come from solar power, representing 35.1% of additions through 2025 with wind energy following closely behind at 32.7%
  The addition of intermittent wind and solar PV resources will further stress transmission systems causing many load serving entities to seek a clean energy dispatchable solution to ensure electric reliability
Renewable capacity additions: 2012-2025
Solar thermal with storage deploys commercially viable technology that can displace fossil fuel generation
Energy storage allows the generator to control a plant’s output and dispatch when electricity is at peak pricing
Storage allows the facility to produce more than twice as much net annual output as solar without storage
Solar thermal with storage can operate like a conventional power plant
Firm output ensures a more stable and secure transmission system
CSP with storage is set to realize falling installation costs as global deployment accelerates
Chart: 
| PV | Wind | Other
Values | 546.94 | 535.15 | 554.89
Chart: 
| Renewable | Fossil fuels | Nuclear
Values | 0.57722 | 0.38188 | 0.040903
Solar PV
547 GW
Wind
535 GW
Other
555 GW
Intermittent renewables
66% (1,082 GW)
Renewable
58%
Fossil
fuels
38%
Nuclear
4%
Global total
capacity additions
2,836 GW
Source: Frost & Sullivan

## Slide 3: Framework: The Value of CSP with Storage
Ancillary Services
  Frequency regulation
  Spinning reserve
  Non-spinning reserve
  Ramping support / load following
  Black start
  CSP with storage delivers multiple value streams which are increasingly important in the changing energy landscape
Intrinsic Stability
  Fault ride-through capability
  Inertia / frequency response
  Voltage / VAR support
Energy and Capacity Value
  Time-shift generation to the highest-value times
  Replace conventional resources for flexibility and reliability
  Higher utilization of transmission assets
  Less fuel / O&M from startup / cycling the fleet
  No “round-trip” losses
Risk Management
  Hedges:
    Power price
    Ancillary service price
    Integration costs
  Improved forecast error
  Lower reserve requirements
  Long-term dispatch flexibility
  Stable lifetime performance and value
Operating Flexibility
  Responsive curtailment
  Slow the net load ramps
  Smooth intra-hour variability
  Ease the integration of intermittent renewables
  Integration with other thermal generators
  Studies have shown how the value of renewables without storage declines as penetration increase
  In contrast, storage allows CSP to deliver superior value over the long term
Curtailment issues and shifting of the net load peak will reduce the value of renewables without storage in the future
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
Geo
Wind
Nuclear
Coal
Imports
Combined cycle
Hydro
Pumped storage
Gas turbine
PV
Base (no PV)
2%
6%
10%
PV penetration and hour
Chart: PV penetration (% annual energy)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 |
NV Power: Perez et al (2008)
CA Case Study: Mills and Wiser (2012)
CA Case Study: Jones (2012)
APA - Tracking: R.W. Beck (2009)
APS - Fixed: R.W. Beck (2009)
WestConnect: GE Energy (2010)
Toronto: Pelland and Abboud (2008)
PGE: Perez et al (2008)

## Slide 4: CSP with Storage: Cost Reduction Opportunities

## Slide 5: SolarReserve CSP Cost Reductions
Chart: 
| Crescent Dunes (2011) | Redstone (2014 Award) | Copiapo (2016 Indicative) | Future Target
Collector Field | 331.2851 | 205.5083 | 177.6351 | 140.1962
MSS & Storage | 155.4528 | 167.3775 | 196.6544 | 133.7073
Power Block | 106.48 | 101.64 | 103.4 | 88.2998
BOP | 66.55 | 72.6 | 60.5 | 60.984
Indirect | 106.882 | 88.6343 | 62.3462 | 46.0216
Soft Costs | 94.3 | 78.2002 | 61.2562 | 37.4903
Financing | 123.57 | 102.473 | 80.2696 | 49.127
Cost (USD $mm)
39% Cost Reduction
Larger collector field, larger receiver and storage to take advantage of higher DNI and baseload requirements
Smaller collector field, slightly higher storage due to capacity & TOD constraints
Cost reductions achieved to date set the platform for future reductions of hard and soft costs

## Slide 6: SolarReserve CSP Cost Reductions: Collector Field Capex Detail
The collector field is a comparatively large part of the overall EPC scope, and has the largest potential for cost reductions through serial production and scale economies
  Structural elements can be reduced without compromising optical quality or durability (e.g., wireless, thinner glass, improved foundations)
Overall soft costs decline further as a result of capex cost reductions
Chart: 
| Facet assembly | Azimuth Drive | Elevation Drive | Control System | Structural Elements | Reduction from CDSEP
 | 30.8798 | 21.8692 | 8.6561 | 18.3178 | 41.1752 | 50
Chart: 
| Facet Assembly | Drive (Dual) | Control System | Structural elements | Reduction from Redstone | Reduction from CDSEP
 | 42.8091 | 24.4027 | 13.8377 | 23.6364 | 16.21 | 50
Crescent Dunes collector field
Redstone collector field
Future collector field advancement
Chart: 
| Facet assembly | Azimuth Drive | Elevation Drive | Control System | Structural Elements | Components EXW
 | 32.505 | 22.7139 | 10.5 | 28.8931 | 87.0449
SolarReserve has achieved significant collector field cost reductions to date,
and has line of sight to 10% additional reduction in the short term
Approximately half of the cost of Crescent Dunes’ heliostats consisted of structural elements
Cost reduction of Redstone’s heliostats achieved primarily through structure steel reduction
Facet improvements further reduce structural requirements

## Slide 7: SolarReserve CSP Cost Reductions: 800°C Receiver
Recipient of CSP APOLLO program award from U.S. Department of Energy SunShot Initiative to develop ceramic receiver that breaks through current temperature and performance barriers, while meaningfully increasing efficiency, energy storage capabilities and lowering capital cost
Partnering Organizations
  UC San Diego
  University of Arizona
Receiver Development Goals
  High outlet temperature to drive higher efficiency supercritical power cycles using thermal storage
  Compatible with Oxy-Chloride molten salts
  30 year life (10,000 thermal cycles)
  90% thermal efficiency
  Affordable capital cost
Result – key component that enables lower cost of electricity (6¢/kWhe)

## Slide 8: SolarReserve CSP Cost Reductions: BOP

## Slide 9
CONTACT INFORMATION
Corporate Headquarters
520 Broadway
6th Floor
Santa Monica, CA 90401
www.SolarReserve.com
Phone: +1.310.315.2200
Toll-Free: +1.866.622.2778
Fax: +1.310.315.2201
Email: Info@SolarReserve.com