## Slide 1: Los Alamos National Laboratory’s Chromium Project
Doug Hintze, Manager
Environmental Management Los Alamos Field Office
January 12, 2018

## Slide 2: Presentation Outline
Frequently asked questions
Chromium facts
Background
Where is the chromium plume?
What is being done about it?
What’s next?
Summary

## Slide 3: Frequently Asked Questions
Is the County’s drinking water safe?
Where did the chromium contamination come from?
Is it still being released to the environment?
Do we know where it is?
What is the Laboratory doing about it?
How does chromium treatment work?
How will the contamination be fully remedied?
What is the timeframe?

## Slide 4: Chromium Facts
Chromium occurs naturally in two forms:
  “Trivalent”
    Considered an essential nutrient (found in vitamins and food)
    Doesn’t move in groundwater
  “Hexavalent”
    “Dissolves” in water and can move in groundwater
    Can change to trivalent chromium either naturally or using remediation approaches
    LANL Chromium plume is hexavalent form
Cooling towers at LANL power plant
Chromium was once used to prevent corrosion in power plant cooling towers

## Slide 5: Chromium in Groundwater Beneath LANL
? ? ? ? ? ?
- - - - -
Chromium (Cr) contamination in the regional aquifer is in hexavalent form
Potassium dichromate used in cooling towers at a Laboratory power plant
Up to 72,000 kg released from 1956-72 in hexavalent form [Cr(VI)]
  3 groundwater zones
  Plume is 900–1,000 feet below canyon bottom in deepest zone
  Size is approximately 1 mile x 1/2 mile x <50 feet thick
  Estimated downgradient plume edge is approximately 1/4 mile from the closest drinking water well
Potassium dichromate used in cooling towers at a Laboratory power plant
Up to 72,000 kg (159,000 lb) released from 1956-72 in hexavalent form [Cr(VI)]
Power Plant
Plume

## Slide 6: Where is the plume?
~1000 feet
Cr Plume
Water Supply Well
Monitoring Well

## Slide 7: Where is the plume? (cont.)
Water-supply well

## Slide 8: What is being done about it?
E
E
E
I
I
I
Extract 
Treat
Inject
T
Hydraulic Control to Prevent Migration
E
I
I?
I?


## Slide 9
Extraction, Treatment & Injection Loop
Extraction Well
Ion Exchange Treatment Unit
Injection Well
INJECTED WATER RESULTS IN MOUNDING OF THE WATER TABLE
Contaminated groundwater is pumped from extraction wells
Groundwater is treated using a method called ion exchange
Clean water is delivered via buried thick-walled piping to injection wells
Water exits the injection wells within the aquifer

## Slide 10: What is being done about it? (cont.)
Approximation of potential plume edge 2-3 years after start up of full system operation of Interim Measure
Groundwater Flow

## Slide 11: What’s next?
Restart operations along Laboratory boundary with Pueblo de San Ildefonso in January
Full system operation summer/fall
Continued studies to evaluate final remedy

## Slide 12
Questions?