## Slide 1: RDX Project
Los Alamos National Laboratory’s RDX Groundwater Project
Los Alamos County Council
Danny Katzman
Technical Manager, Water Programs – N3B
February 5, 2019

## Slide 2: RDX Project – Presentation Topics
Presentation Topics
Background
  Groundwater setting
  Source and history
  Remediation conducted to date
Extent of RDX in groundwater
Next Steps

## Slide 3: Groundwater beneath Los Alamos
~1300 feet to the water table
Typical Water-Supply Well
Regional Aquifer Monitoring Well
Perched Groundwater Monitoring Well
Spring

## Slide 4: Background
TA-16 facilities established in early 1950s to develop high explosive (HE) formulations
  Explosives (RDX, HMX, TNT) were casted and machined for nuclear weapons in 260 Bldg starting in 1951
  Several million gal/yr of HE-contaminated water discharged to Caon de Valle (CdV) between 1951 – 1996
First investigations of RDX in soils occurred in the mid 1990s
Groundwater investigations first identified RDX (below standard) in perched and regional groundwater in the late 1990s
Present-day RDX contamination is low in nearby springs, surface water, and shallow groundwater
Current estimates of RDX in environment:
  ~ 1500 – 3600 kg total;
  ~ 35 – 415 kg in regional aquifer
260 Outfall
TA-16
TA-9

## Slide 5: RDX Remediation Activities
Surface soil cleanup conducted in outfall area in 2000 – 2001 under an Interim Measure, and in 2009 – 2010 under a Corrective Measures Implementation
  More than 1500 yd3 HE-contaminated soil excavated and disposed offsite
  Significantly reduced contamination in surface soils
Injected grout in permeable rock layers to cut off infiltration pathways
Remedy Completion Report - 2017
  Documentation of no further action necessary for cleanup for RDX in surface setting
  Long-Term Monitoring Plan and reporting requirements for surface water, springs, shallow alluvial wells

## Slide 6: Deep Groundwater Activities
Installation of monitoring wells to investigate “nature and extent” of contamination
  Depth to regional aquifer is approximately 1300’ below ground surface in the TA-16 area because of the elevation of the mesas in the area
  Including the latest monitoring well, R-69, there are 9 wells used to monitor the regional groundwater in the RDX area
  Intermediate-depth wells screened in perched groundwater (~600-1000 ft bgs)
  Deep wells screened in the regional aquifer (~1200-1400 ft bgs)
Studies to understand the hydrology and “fate and transport” of contamination
  Tracer studies
  Aquifer tests
  Groundwater flow ~20 – 40 ft/yr; RDX in groundwater slightly slower
All investigation activities performed with NMED’s approval

## Slide 7: Conceptual Model
RDX Pathway

## Slide 8: RDX in Regional Aquifer
RDX is present in several regional groundwater monitoring wells
Known since 1998
Two monitoring wells (R-68 and R-69) have RDX above the NMED’s 7.02 ppb tap-water screening level
  R-68 ~ 14 ppb
  R-69 TBD
RDX is not present in LAC water-supply wells (approx. 3 miles away)
DOE collects groundwater samples from water-supply wells for RDX analysis
  sampled since 1998
  Current semi-annual sampling supplements LAC’s sampling efforts
DOE/N3B will continue to monitor for RDX in water-supply wells and in monitoring wells closer to the RDX project site
~ 3 miles

## Slide 9: Upcoming Activities
Deep Groundwater Investigation Report (DGIR)
  Due to NMED in August 2019
DGIR Objectives
  Is the contamination sufficiently characterized?
  A groundwater model will evaluate
    Potential for long-term migration of RDX in regional aquifer (i.e., predictions for whether the footprint could grow)
    whether groundwater remediation is necessary
    If remediation is necessary, a plan will be developed to propose the approach
  Long-term monitoring to ensure protection of LAC water-supply wells will be part of any path forward
All activities conducted under the Consent Order with NMED

## Slide 10: Approximate Schedule of Activities
Corrective
Measures Evaluation
Investigation Report
NMED Review
8/19
Corrective
Measures Implementation Plan
~ 2/20
8/20
9/21
Long-Term Monitoring
?
?
Ongoing Monitoring

## Slide 11
Questions?