## Slide 1
Presentation to Regional Coalition of LANL Communities
December 21, 2018
Joe Legare
Acting Chief Operating Officer
N3B Los Alamos

## Slide 2
Agenda
N3B Overview
RDX Campaign Project Overview

## Slide 3: N3B Los Alamos: How We Support LANL
Triad National Security
Notes: Los Alamos National Laboratory is managed by two Department of Energy organizations:
National Nuclear Security Administration
Environmental Management
EM has been responsible for cleanup work at LANL for several years, with the lab M&O contractor doing the work – until May of 2018, when the work was spun off from the M&O to form the Los Alamos Legacy Waste Contract, which N3B manages.
Our sole purpose at Los Alamos is to clean up the site’s legacy waste.

## Slide 4: N3B Los Alamos: Who We Are
Cleanup up the Environment – Protect our Future
Notes: N3B is a limited liability company that is owned by Huntington Ingalls Industries and BWX Technologies.
Our major teaming subcontractors are Tech 2 Solutions and Longenecker & Associates.

## Slide 5: N3B Mission – Values - Scope
N3B Mission
To manage and execute the Los Alamos Legacy Cleanup Contract (LLCC) safely, securely, compliantly and efficiently to the satisfaction of our customers and stakeholders while adhering to disciplined operations principles.
Core Values
Safety
Integrity
Quality
Performance
Stewardship
Communication & Collaboration
Major Scope Areas
Excavate, treat, package and ship waste
Excavate soil and buried components, package and dispose
Close landfills
Comply with groundwater and surface water permits
Treat groundwater
Decontaminate and demolish facilities
Communicate with Regulators, Stakeholders and local elected officials
Notes: We are organized to safely, securely, compliantly and efficiently:
Manage groundwater and surface water and treat as necessary
Clean up and close waste sites
Demolish facilities
Excavate, treat, package and ship waste for dispsoal

## Slide 6: N3B Organization
Erich Evered (Acting)
Adam Barras
Mike Helpenstill (Acting)
Notes: We report directly to the Department of Energy and not to the Lab or the Lab M&O.
Nick Lombardo is president of N3B and Program Director for the Los Alamos Legacy Cleanup Contract.
You may already have met several of our senior leadership, including Frazer Lockhart and others who have added meetings and presented to this group.

## Slide 7
RDX Campaign Project Overview
December 21, 2018
Pat McGuire
RDX Project Lead
N3B Los Alamos

## Slide 8: Presentation Topics
Background
  Groundwater setting
  Source and history
  Remediation and monitoring conducted to date
Extent of RDX in groundwater
  Water supply wells do not contain RDX
  DOE has a program in-place with the goal that RDX will not be present in the water supply wells
Upcoming Activities

## Slide 9: Groundwater beneath Los Alamos
~1300 feet
Water-Supply Well
Regional Aquifer Monitoring Well
Perched Groundwater Monitoring Well
Spring

## Slide 10: Background
TA-16 facilities established in early 1950s to develop high explosive (HE) formulations
  Explosives (RDX, HMX, TNT) were casted and machined for nuclear weapons
  Building 260 used since 1951 to machine HE
  Several million gal/yr of HE-contaminated water discharged to Caon de Valle (CdV) between 1951 – 1996
  The 260 Building outfall was primary source of RDX
  Other potential sources include operations in other buildings at TA-16 and at TA-09.
First investigations of RDX in soils occurred in the mid 1990s
Groundwater investigations first identified RDX (below standards) in perched and regional groundwater in the late 1990s
Present-day RDX contamination is low in nearby springs, surface water, and shallow groundwater
260 Outfall
TA-16
TA-9

## Slide 11: Remediation Activities Conducted
Surface soil cleanup conducted in outfall area in 2000–2001 under an Interim Measure, and in 2009–2010 under a Corrective Measures Implementation
  More than 1500 yd3 HE-contaminated soil excavated and disposed offsite
  Significantly reduced contamination in surface soils
  Excavations backfilled with clean soil and covered with a stone cap
Completed Surface Corrective Measures Activities
  Included documentation of no further requirements for cleanup for RDX in surface setting
  Included Long-Term Monitoring Plan and reporting requirements
  Surface water, springs, shallow alluvial wells

## Slide 12: Deep Groundwater Activities
Installation of monitoring wells to investigation “nature and extent” of contamination
  Including the latest monitoring well, R-69, there are 9 wells used to monitor the regional groundwater underlying TA-16 and TA-9
  Intermediate-depth wells screened in perched groundwater (~600-1000 ft bgs)
  Deep wells screened in the regional aquifer (~1200-1400 ft bgs)
Studies to understand the hydrology and “fate and transport” of contamination
  Tracer studies
  Aquifer tests
All investigation activities performed with NMED’s approval

## Slide 13: Groundwater Flow Conceptual Model
RDX SOURCE

## Slide 14: RDX in the Regional Aquifer
RDX is present in several regional groundwater monitoring wells
Known since 1998
Two monitoring wells (R-68 and R-69) have RDX above the NMED’s 7.02 ppb screening level (protective risk based concentration)
RDX is not present in LAC water-supply wells (approx. 3 miles away)
DOE collects groundwater samples from water-supply wells for RDX analysis
  sampled since 1998
  Current semi-annual sampling supplements LAC’s sampling efforts
DOE will continue to monitor for RDX in water-supply wells and in upgradient monitoring wells closer to the RDX project site

## Slide 15: Upcoming Activities
Deep Groundwater Investigation Report (DGIR)
  Due in August 2019 (Consent Order “Appendix B” Deliverable)
Field Activities to support DGIR
  R-69 installation of sampling equipment, monitoring
DGIR Path Forward
  DGIR will include a groundwater model that will
    Model long-term fate of RDX in regional aquifer
    Determine whether groundwater remediation is necessary at this time to protect regional aquifer
Long-term monitoring will follow
All activities performed in collaboration with NMED