## Slide 1: Report Writing
QUALITY CONTROL INSPECTOR
WEATHERIZATION ASSISTANCE PROGRAM STANDARDIZED CURRICULUM – September 2012

## Slide 2: Learning Objectives
By attending this session, participants will be able to:
Discuss the purpose of various reports.
Describe the kinds of information to include in specific reports.
Identify tips for writing a clear, concise, and useful report.
Recognize and address patterns and trends.
Explain how the tone of a report can affect worker morale and motivation.
REPORT WRITING
Notes: By attending this session, participants will be able to:
Discuss the purpose of various reports.
Describe the kinds of information to include in specific reports.
Identify tips for writing a clear, concise, and useful report.
Recognize and address patterns and trends.
Explain how the tone of a report can affect worker morale and motivation.

## Slide 3: The Purpose of Reporting
Audit, monitoring, and inspection reports ensure the WAP operates effectively and efficiently.
Measures are implemented correctly.
Funds are spent wisely.
Reports verify program oversight.
Reports can recommend training and technical assistance (T&TA) where needed.
Reports can be used to compile data for national program evaluations.
REPORT WRITING
Notes: Audit, monitoring, and inspection reports are necessary to ensure WAP operates effectively and efficiently.
Measures are implemented correctly.
Funds are spent wisely.
Reports demonstrate that program oversight was conducted per program requirements.
Reports can recommend training and technical assistance (T&TA) where needed.
Reports can be used to compile data for national program evaluations.

## Slide 4: Inspection Reports
Inspection reports:
Fulfill a WAP requirement.
Document that appropriate and allowable measures are installed in WAP units.
Confirm the weatherization work completed in a dwelling was what was recommended within the audit or priority list.
REPORT WRITING
Notes: Inspection reports:
  Fulfill a WAP requirement for program oversight.
  Document appropriate and allowable measures installed in WAP units.
  Confirm the weatherization work completed in a dwelling was what the auditor recommended or the priority list allows.
Program regulations require inspections of all weatherized units.
It is best if the inspector and the auditor are not the same person and the inspector is not inspecting work that s/he called for in the first place. This prevents conflicts of interest and retains an independent check and balance process.
Like the audit report, the local agency’s inspection report may be based on a standard form that a subgrantee uses or a grantee requires.

## Slide 5: Inspection Reports
Document post-weatherization test results.
Verify billing was correct and everything billed was actually installed in the dwelling.
Confirm quality workmanship on every WAP unit.
Identify poor workmanship and maintain tracking record of “call-backs” and re-inspections by the local agency inspector.
Result in sign-off by final inspector as a completed WAP unit to be reported for production goals.
REPORT WRITING
Inspection reports should:
Notes: Inspection reports should:
  Document post-weatherization test results.
  Verify billing was correct and everything billed was actually installed in the dwelling.
  Confirm quality workmanship on every WAP unit.
  Identify poor workmanship and maintain a record of call-backs and re-inspections by the local agency inspector.
  Eventually result in a sign-off by the final inspector as a completed weatherized unit that may be counted toward production goals.
Inspectors should perform post-weatherization testing in areas where pre-weatherization tests were conducted (e.g., blower door, combustion safety, pressure pan).
Payment can’t be made until the inspector puts his/her signature on the inspection report. Verifying the billing is correct is as important as ensuring that quality workmanship was performed.
The inspector should be able to identify any problems with installations or missed opportunities based on the auditor’s recommendations. The inspector should initiate a call-back of a crew or contractor, if necessary.

## Slide 6: Inspection Report Format
Inspection reports generally follow a structured format.
Inspectors fill in information on the inspection form.
There is generally not a large amount of text narrative.
The inspection report indicates if measures were installed as required, and if any rework is required.
REPORT WRITING
Notes: Inspection reports generally follow a structured format.
Inspectors complete the inspection form, which basically constitutes the report. Generally, there is not much text.
Most inspectors use inspection forms they complete in the field. Generally, all inspectors for a grantee use the same forms.
Inspection forms may vary across subgrantees in a state or they may be uniform if a grantee requires them to be so.
Most inspection reports have notes sections for text. Additional pages can be added if necessary.

## Slide 7: Tips for Inspection Reports
Review the audit report and address any special issues the auditor mentions.
Be as thorough as possible.
Use complete sentences.
Detail why any measures the auditor recommended were not implemented.
Note the quality of workmanship observed at the dwelling. Issues related to particular measures should be noted individually.
Use good penmanship!
REPORT WRITING
Notes: Review the audit report, and address any special issues the auditor mentions. Be as thorough as possible in documenting the work performed.
Use complete sentences to express thoughts and when providing instructions.
Inspection reports should detail why any measures the auditor recommended were not implemented.
Inspection reports should detail the quality of workmanship observed at the dwelling. Issues related to particular measures should be noted individually.
Because inspection reports are completed in the field, legible handwriting is important to ensure no one misinterprets the report.

## Slide 8: Patterns
II. Severe kink
III. Hole
I. Minor kink
REPORT WRITING
Photos courtesy of US Dept. of Energy
Notes: These photos show the backs of clothes dryers and the walls through which they are vented. Each vent has a problem that was created when the installer pushed the dryer back into position. None of these dryer vents meet the intent of the program.
Photo I: A minor restriction from the vent duct being squeezed slows air movement through the dryer, increasing drying time.
Photo II: A major restriction from the vent duct being squeezed further increases drying time. This will shorten dryer life and can create a fire hazard.
Photo III: A major restriction increases drying time. A hole cut in the vent duct allows moisture and wash chemicals free access to the home’s interior, reducing indoor air quality (IAQ).
If a community action agency (CAA) final inspector took these pictures during a final inspection, s/he could recommend the installer get training in proper dryer venting methods and materials, and the crew chief get training in checking the installer’s work.
If the pictures came from a state-level monitoring of homes weatherized by a single CAA, the problem is systematic. The auditor, inspector, crew chief, installer, and any other on-site personnel the CAA employs need training in proper dryer venting methods and applicable house-as-a-system science.
Your report should be based on patterns of unacceptable work. The dryer vent installations pictured are deficient in similar ways. A single error or oversight may simply mean someone had a bad day. If several houses in a sample have similar failings, the problem is most likely either a need for additional training or a lack of understanding of why a particular task is important.
Frequently, there are patterns of improper measures in any sample of houses:
Multiple missed chimney bypass seals.
Poor workmanship on attic hatch treatments.
Repeated improper installation of door weatherstrips.
Q: When does a pattern become a trend?
A: Generally, a pattern refers to a series of similar events in a limited sample, while a trend is an entity-wide practice.

## Slide 9: Trends
Photo I.
Hole in door skin
Photo II.
Photo III.
Photo IV.
REPORT WRITING
Photos courtesy of US Dept. of Energy
Notes: A trend is more pervasive than a pattern. One example of a problematic trend would be a particular CAA weatherization program installing large numbers of replacement windows and doors rather than insulating walls.
Training to reinforce or discourage trends is generally limited to auditors and inspectors and consists mainly of explaining DOE requirements concerning savings-to-investment ratio (SIR) calculations and individual measures prioritization.
The doors pictured, from left to right, are:
Photo I: An insulated core 2¼-in. thick wooden door to be replaced because of the hole in the exterior skin below the center window – There will be no appreciable savings from replacing this insulated core door with even the best available replacement door.
Photo II: A 2-in. thick pine door being replaced because of the single-pane glass – Note the doorway has a metal storm door in good condition. Replacing a good primary door/storm door assembly (with an R-value of R-2 or R-3) with a typical replacement door (R-5 at best) will produce very little savings at high cost, likely resulting in a negative SIR.
Photo III: A replacement insulated steel door – This new door has been installed in an exceedingly rundown inner city property. It is quite unlikely the building will stand long enough to achieve a positive SIR.
Photo IV: A replacement insulated steel door with window – According to the client, this new door replaced a wooden door with an aluminum storm. It appears that like was replaced with like (R-2+ with R-2+), eliminating any possibility of a positive SIR.
The door replacements were ordered by different auditors at the same CAA. The CAA employing the auditors has a reputation for installing at least one door in nearly every home it weatherizes.
If a CAA inspector took these pictures during a final inspection, s/he could recommend the auditor get training to understand DOE requirements concerning SIR.
If the pictures came from a state-level monitoring of weatherized units from a single CAA and is typical of its work, then the pervasive door replacement may be a high-level policy decision. If that is the case, the CAA weatherization director needs training in the intent of the DOE WAP, SIR requirements, and program management.

## Slide 10: Report Tone, Exercise #1
Photo I.
Photo II.
Photo III.
Photo IV.
REPORT WRITING
Photos courtesy of US Dept. of Energy
Notes: Refer to Lesson Plan  Exercise # 1. (20 minutes)
All the pictured attic hatches were installed or upgraded by the same CAA crew.
Photo I: The crew installed molding and a weatherstrip around the hatch opening.
Photo II: The crew installed a weatherstrip and insulation on the upper side of the hatch, which is a client-installed cabinet door hinged to the ceiling and held closed by a turn button.
Photo III: The crew built a hatch from scratch using molding supplied by the client to match the existing molding.
Photo IV: The crew installed a weatherstrip around the existing hatch.
Three of the four pictured hatches failed the Any Town CAA final inspection. Which hatches failed and why?
Photo I: Fails  The lid is warped and doesn’t contact the weatherstrip. The new molding is not sealed or painted to match the existing molding.
Photo II: Fails  A recycled cabinet door over a ragged hole is not a proper hatch. The weatherstrip installed by the crew provides an insufficient air seal between the door and the broken plaster ceiling above.
Photo III: Fails  The client-supplied molding was poorly fitted by the crew. The mitered joints are not air sealed.
Photo IV: Passes  This looks nice. The weatherstrip is air tight, as determined by a blower door test.
After reviewing these examples of acceptable and unacceptable work, ask the students to think about how they would present that work in their reports. Discuss the appropriate tone for a report and why tone matters. Reinforce the following:
Be positive.
Be concise.
Don’t nitpick.
Write as if you were the recipient.

## Slide 11: Creating a Report
Review site visit “paper.”
Create report outline.
Flesh out report.
Summarize important points.
Suggest training needs and opportunities.
Praise exceptional work.
File all field notes, draft reports, pictures, etc.
REPORT WRITING
Notes: When creating a report, be sure to:
Review site visit forms, field notes, and pictures.
Develop an outline.
Organize by individual units.
Address units in the order visited.
List measures installed on each unit.
List any other pertinent information, such as blower door numbers.
Flesh out the report. Be brief, using bullet points when possible.
Start each unit section with a picture of the unit.
Include a list of installed measures.
  Note which measures were installed well and which need improvement.
  Include pictures supporting individual measure observations.
Record any client comments.
Summarize important patterns and trends.
Suggest training needs by title, not by name.
Note peer training opportunities.
Record exceptional work.
File all paperwork, including field notes, pictures, and report drafts in case you need them later.
The CAA may question the report’s conclusions.
If you need to summarize activities during the grant period, they will be a valuable resource.
In the event of legal action, these documents will be important evidence.

## Slide 12: Exercise #2
Photo I.
Photo II.
Photo III.
REPORT WRITING
Photos courtesy of US Dept. of Energy
Notes: Refer to Exercise 2 in Lesson Plan (20 minutes).

## Slide 13: What to Look for in Audit Reports
Audit reports should:
Document the findings of the auditor during the initial visit to the dwelling.
Document any pre-weatherization test results.
Recommend measures to be implemented.
Explain unique or difficult issues to installation technicians.
REPORT WRITING
Notes: This course is not designed for auditors; but as final inspectors and monitors work closely with auditors, an overview of audit reports is provided for your convenience.
Audit reports:
  Document the auditor’s findings during the initial visit to the dwelling.
  Document any pre-weatherization test results.
  Recommend measures to be implemented.
  Explain unique or difficult issues to installation technicians.
Audit reports are a required element of the Weatherization Assistance Program (WAP).
A unit can’t be weatherized until an auditor has evaluated it.
The audit report highlights the measures recommended by the auditor based on either the audit or the priority list. The auditor’s notes become the roadmap to implementation.
An audit report records all pre-weatherization testing the auditor conducted:
  Blower door cubic feet per minute (CFM) readings.
  Combustion safety readings.
  Pressure pan readings.

## Slide 14: Audit Reports
Audit reports generally follow a pre-determined format.
Auditors fill-in information on the audit form.
There is generally not a large amount of text.
Sample NEAT Audit recommended measures produced from auditor’s inputs after field assessment.
REPORT WRITING
Notes: Audit reports generally follow a pre-determined format. Most auditors use audit forms they complete in the field. All auditors employed by a given subgrantee use the same forms.
Auditors fill in information on the audit form, which basically constitutes the report. Audit forms may vary across subgrantees in a state or they may be uniform if a grantee requires them to be so.
Generally, there is not a large amount of text. Most audit reports have notes sections for text. Additional pages can be added if necessary.

## Slide 15: Exercise #3
Exercise #3
(40 minutes)
Notes: Refer to Exercise #3 (40 minutes).

## Slide 16: Summary
Audit, monitoring, and inspection reports are necessary to ensure WAP operates effectively and efficiently.
Reports provide a record of program performance.
Organize reports chronologically.
Keep reports positive.
Praise good work.
Summarize patterns and trends.
Recommend training by title, not name.
Keep good records!
REPORT WRITING
Notes: Audit, monitoring, and inspection reports are necessary to ensure WAP operates effectively and efficiently.
Reports provide a record of program performance.
Organize reports chronologically.
Keep reports positive.
Praise good work.
Summarize patterns and trends.
Recommend training by title, not name.
Keep good records!
Present this slide as an interactive discussion, soliciting personal examples from the trainees. Add your own personal examples and knowledge to supplement.